| Fuel Injection > A/C Clutch |  |
| --- | --- |

| Secondary Air Injection | Electric Cooling Fan |
| --- | --- |

A/C Clutch

To improve idle quality and WOT performance, the PCM controls engagement of the A/C clutch on some systems (figure 4-49). At idle, the PCM first commands the IAC valve to increase engine idle slightly, then grounds the A/C relay. This minimizes poor idle quality or stalling. The PCM will interrupt A/C operation at wide-open throttle, when maximum engine performance is desired. When the power steering pressure (PSP) switch signals high power steering pressure at low engine speed (during parking, for instance), the PCM removes the ground from the A/C clutch relay to prevent stalling caused by the compressor load on the engine. If engine cooling system overheating is indicated by the coolant temperature sensor, A/C operation is interrupted.

Figure 4-49, A/C Clutch Control Circuit